## Slide 1
REMOTE SENSING–BASED DETECTION AND TRACKING OF MARINE LITTER
(EMPHASIS ON MACRO PLASTIC) ALONG THE INDIAN COAST
JRF:
Kaushal Nileshbhai Maniyar
Under Guidance:
Dr. Madhuri Bhavsar (PI)
Dr. Sudeep Tanwar, Dr. Swati Jain
Dr. Jaiprakash Verma, Dr. Madhukant Patel
Focal Persons (SAC/ISRO):
Dr. Jishad M., Dr. Aditya Chaudhary,
Dr. Surisetty V. V. Arunkumar, Dr. Neeraj Agrawal
Institute of Technology, Nirma University

## Slide 2
PROBLEM BACKGROUND & MOTIVATION
Plastic makes up 60–80% of global marine litter — up to 95% in coastal hotspots.
India has a 7,500+ km coastline; rivers such as the Cooum and Ganga are major plastic outflows to the ocean.
Manual monitoring (boats, drones) is costly and spatially limited.
Satellites enable large-scale, low-cost, repeat observation of floating litter.
Goal: Build an AI/ML pipeline to detect floating plastic from multispectral remote sensing data.

## Slide 3
PROJECT OBJECTIVES
1. Study floating marine debris using remote-sensing optical data.
2. Spectrally characterize plastic and build a spectral library.
3. Develop AI/ML models to automatically distinguish plastic from water, vegetation, sediment, etc.
4. Validate on satellite (Sentinel-2) imagery and real coastal sites.
Target: Detect plastic even at ≥1% pixel coverage — the smallest realistic signal at satellite resolution.

## Slide 4
METHODOLOGY — END-TO-END PIPELINE
Data Sources
• Hyperspectral spectrometer (Exp 1) — 469 samples, 1%–100% pixel coverage.
• Reve multispectral sensor (Exp 2) — 18 bands, 410–940 nm, 79 → 400 samples (SMOTE).
• MADOS / Sentinel-2 satellite (Exp 3) — 2,803 images, 15 classes, ~1.5 M annotated pixels.
Processing Pipeline
• Preprocessing: reflectance normalization, ACOLITE atmospheric correction.
• Feature engineering: NDVI, FDI, proposed Sea Snot Index (SSI).
• Class balancing: SMOTE.
• Models: SVM, RF, MLP, kNN, AdaBoost, 1D-CNN, 1D-CNN + Transformer, Self-supervised.
• Post-processing: DBSCAN, Closing, Modulo Filter, SAM segmentation.

## Slide 5
EXPERIMENTS OVERVIEW
Exp 1 — Hyperspectral Spectrometer
Data: 469 samples (262 plastic) · pixel coverage 1–100% · water / sediment / vegetation.
Best model: 1D CNN + Transformer — 97% overall · 100% at 1% pixel coverage.
Exp 2 — Reve Multispectral (410–940 nm, 18 bands)
Data: 79 → 400 samples after SMOTE · outdoor + indoor.
Best models: SVM & MLP — 100%; AdaBoost 99%; RF 98% (using NDVI + 940 nm).
Exp 3 — MADOS / Sentinel-2 (real satellite data)
Data: 2,803 images, 15 classes, ~4,696 Marine Debris pixels.
Best model: SVM — Recall 0.83 (pixel), 0.98 (image); Precision improved via post-processing.

## Slide 6
EXPERIMENT 1 — HYPERSPECTRAL CHARACTERIZATION
Design
• Custom test-pad; 30° spectrometer FOV; 5.75-inch target radius.
• 469 spectra — 262 plastic (multi-color, transparent) + water, sediment, vegetation, soil, iron, concrete.
• Pixel coverage sweep: 1%, 25%, 50%, 75%, 100%.
Key Results
• 1D CNN + Transformer — 97% overall accuracy, 100% at 1% pixel coverage.
• Random Forest 90%; SVM (trained) 96%; raw SVM failed (0%).
• Spectral normalization removed time-of-day variation (morning vs. evening).
• SHAP highlighted a small set of wavelengths that drive plastic classification.
Key Insight
• Models trained on one sensor did not transfer to another — must train per target sensor.

## Slide 7
EXPERIMENT 2 — REVE MULTISPECTRAL (410–940 nm)
Design
• 18-band Reve sensor; indoor + outdoor (Charodi Lake, Nirma campus).
• 9 object classes; 79 raw samples → 400 after SMOTE oversampling.
Feature Engineering
• NDVI (Landsat-8 analogue): (R860 − R645) / (R860 + R645).
• FDI adapted: (R810 + (R900 − R810)·0.56) − R860.
• Empirical study → NDVI + 940 nm separates plastic vs. non-plastic cleanly (2D scatter).
Results (All bands + NDVI)
• SVM & MLP — 100% · AdaBoost 99% · RF 98% · kNN/DT 97% · GNB 95%.
• Self-supervised (encoder-decoder + RF): 0.87 – 0.96 across seeds.

## Slide 8
EXPERIMENT 3 — MADOS / SENTINEL-2
Dataset & Scale
• 2,803 Sentinel-2 images (240×240), 15 classes, ~1.5 M annotated pixels.
• 4,696 Marine Debris pixels; 7.6 L train / 3.5 L val / 3.6 L test pixels.
Pixel-level Results (SVM, best of 6 models)
• Recall 0.83 · Precision 0.60 · F1 0.70 (MD class).
Image-level Results (SVM, full dataset)
• TP 121 · FP 194 · TN 405 · FN 2 · Recall 0.98 · Precision 0.38 · F1 0.55.
• High recall, but false positives from ships / islands / Sea Snot drag precision.

## Slide 9
IMPROVING PRECISION — SSI & POST-PROCESSING
Sea Snot Index (proposed)
• SSI = (R_B8 − R_B11) / (R_B8 + R_B11) — targets the spectral gap of sea snot.
• Motivation: sea snot was the largest source of false positives.
Post-processing — Image-level F1 on MADOS
• SVM baseline Recall 0.98 · Precision 0.38 · F1 0.55
• + Closing (3×3) Recall 0.05 · Precision 0.31 · F1 0.09
• + Modulo Filter (2×2) Recall 0.48 · Precision 0.49 · F1 0.48
• + SAM (Meta) Recall 0.69 · Precision 0.42 · F1 0.52
• Takeaway: SAM best balances recall & precision; closing over-erodes small debris.

## Slide 10
FIELD VALIDATION — REAL SENTINEL-2 SITES
Sites Tested
• Limassol Bay (Cyprus) — plastic-net target (Jun 2025).
• Cooum River, Chennai — urban plastic outflow (Jun 2022).
• Ocean CleanUp Interceptors — river-mouth debris capture sites (Jan 2025).
Observations
• Model correctly localises debris patches; morphology preserved after SAM.
• Initial accuracy poor without atmospheric correction.
• After ACOLITE correction: predictions cleaner, noise drastically reduced.
• ACOLITE integration currently blocked by a ‘NoneType’ pre-processor error — in progress.

## Slide 11
KEY INSIGHTS
1. Plastic is detectable at ≥1% pixel coverage — 1D CNN + Transformer generalises across coverage levels.
2. NDVI + 940 nm is a surprisingly strong 2-feature separator at multispectral resolution.
3. Sea snot is the dominant false-positive class; a dedicated SSI helps but is not a full fix.
4. Post-processing trades recall for precision — SAM segmentation is the best compromise.
5. Atmospheric correction (ACOLITE) is non-negotiable for real Sentinel-2 scenes.
6. Cross-sensor transfer fails — models must be trained on data from the target sensor.

## Slide 12
CONCLUSION
• Delivered a full pipeline: spectrum → features → ML/AI → post-processing → satellite deployment.
• Three complementary experiments covering sensor, platform and scale.
• 97–100% accuracy on controlled spectra; 0.98 recall on real MADOS imagery.
• Proposed a novel Sea Snot Index to attack the main false-positive source.
• Validated end-to-end on three real coastal sites with Sentinel-2 data.
Outcome: A deployable, India-ready framework for satellite-based plastic monitoring.

## Slide 13
FUTURE WORK
Short term
• Resolve ACOLITE pipeline error; integrate as an automated preprocessing step.
• Retrain detection models on Sentinel-2 bands to close the cross-sensor gap.
Medium term
• Release an open hyperspectral library of Indian plastics + environments.
• Extend the Sea Snot Index and test deep segmentation models (U-Net, DeepLabv3+).
Long term
• Operational deployment along the Indian coast; integrate with ISRO Sentinel-2 products.
Ask: access to SAC / ISRO Sentinel-2 archive for target sites along the Indian coast.

## Slide 14
THANK YOU