## Slide 1
REMOTE SENSING–BASED DETECTION AND TRACKING OF MARINE LITTER
(EMPHASIS ON MACRO PLASTIC) ALONG THE INDIAN COAST
JRF:
Kaushal Nileshbhai Maniyar
Under Guidance:
Dr. Madhuri Bhavsar (PI)
Dr. Sudeep Tanwar, Dr. Swati Jain
Dr. Jaiprakash Verma, Dr. Madhukant Patel
Institute of Technology, Nirma University

## Slide 2
PROBLEM BACKGROUND & MOTIVATION
  Marine plastic pollution is a major global threat; plastic constitutes 60–80% of marine litter, reaching up to 95% in some regions.
  Plastic debris affects marine life, human health, and coastal ecosystems.
  Manual monitoring using boats/drones is limited; satellite-based approaches offer large-scale, cost-effective monitoring.
  Goal: Develop AI/ML-based methods to detect floating plastic using multispectral remote sensing data (Reve Spectrometer & Sentinel-2).

## Slide 3
METHODOLOGY OVERVIEW
Data Sources
  Controlled experiments with Reve Spectrometer (410–940 nm, 18 bands).
  Natural sites: Bopal Canal, Charodi Lake, and Nirma campus.
  Real satellite data from the MADOS dataset (Sentinel-2).
Processing Pipeline
  Reflectance normalization
  Feature engineering (NDVI, FDI, SSI)
  Balanced dataset via SMOTE
  Model training: ML (SVM, RF, MLP, kNN) & Deep Learning (1D-CNN, CNN+Transformer)
  Post-processing: DBSCAN, Closing Operation, Modulo Filter, SAM

## Slide 4
EXPERIMENTS AND KEY RESULTS
Experiment 1 (Spectrometer Dataset)
  26 plastic + 53 non-plastic samples.
  Empirical finding: NDVI + 940 nm most effective features.
  SVM & MLP achieved 100% accuracy, RF: 98%, AdaBoost: 99%.
  Shows plastic can be separated even with minimal signal variability.
Experiment 2 (Extended Spectral Data, 469 samples)
  Multi-environment, multi-coverage (1% to 100%).
  Hybrid 1D CNN + Transformer achieved 97% accuracy.
  SHAP analysis identified key wavelengths driving plastic detection.

## Slide 5
MADOS DATASET STUDY & FIELD VALIDATION
  Focus on real-world floating plastic detection using Sentinel-2 imagery.
  SVM achieved Recall 0.98 for marine debris class, but false positives occurred due to Sea Snot / organic matter.
  Proposed a new Sea Snot Index (SSI) — limited but helpful.
  Post-processing (DBSCAN, Modulo Filter, SAM) significantly improved localization.
Real-site Evaluation
  Initial testing gave poor results due to missing atmospheric correction.
  After ACOLITE preprocessing, results improved drastically with cleaner predictions and reduced noise.

## Slide 6
CONCLUSION & FUTURE WORK
Conclusion
  Developed a robust pipeline for spectral characterization + ML/AI detection of floating plastic.
  Achieved high accuracy across controlled and satellite-based datasets.
Future Work
  Large-scale operational deployment along the entire Indian coast.
  Further optimization of SSI and deep-learning segmentation models.

## Slide 7
THANK YOU